|  | POW-105 | POW-107BBT (SP) | POW-107BBT | POW-109BC |
| --- | --- | --- | --- | --- |
| 1. Input Voltage ± 10% | 220V AC | 220V or 110V AC Switchable | 220V | 220V AC |
| 2. Output Voltage | 13.8V DC | 11 – 15V DC 13.8V DC Default | 11 – 15V DC 13.8V DC Default | 1-15V DC Variable |
| 3. Voltage Regulation | X | Fully regulated | Fully regulated | Fully regulated |
| 4. Short Circuit Protection | √ | √ | √ | √ |
| 5. Over Voltage Protection on Output | X | √ | √ | √ |
| 6. Internal Battery Option for Mains Fail | X | √ | √ | X |
| 7. Low Battery Voltage Cut Out | X | √ | √ | X |
| 8. Output Current | 3 – 5 amps | 10 – 12 amps | 10 – 12 amps | Max 30 amps |
| 80% Standby – 20% Full Load | 80:20 Duty Cycle | 80:20 Duty Cycle | 80:20 Duty Cycle | 80:20 Duty Cycle |
| 9. Operating Temperature | -10 to + 60 °C | -10 to + 60 °C | -10 to + 60 °C | -10 to + 60 °C |
| 10. Ripple and Noise | < 100 mV P-P | < 80 mV P-P | < 80 mV P-P | < 1 mV P-P |
| 11. Type | Linear | Toroidal | Toroidal | Toroidal |
| 12. Size |  | 170mm width 110mm height 230 mm length | 170mm width 110mm height 230 mm length | 175mm width 150mm height 250mm length |
| 13. Thermal Cut Out (Self Restoring) | X | √ | √ | √ |
| 14. Charge Over-current Circuit Breaker | X | X | X | √ |
| 15. Metering | X | Analogue Voltmeter and Ammeter | Analogue Voltmeter and Ammeter | Analogue Voltmeter and Ammeter |

# Text boxes

POWER SUPPLY SPECIFICATIONS